IXP Training Part 2 Outline

First Hour

- Packet Counter Project – 1ME Version

- Demo how to simulate packet traffic

- Explain the base project

- Using “Shared GPR” to implement the counter.

- Explain the reason of using “shared” GPR

Subset of the real counter value

- Show that the design is valid

The execution of thread is non-preemptive

- Demo how to allocate multiple ME to packet processing

- The design will not result in the correct one when multiple ME are used

- Packet Counter Project – Multiple ME Version

- Code for allocating a scratchpad variable

static __declspec(scratch) unsigned int *pkt_count = (__declspec(scratch) unsigned int *)SCR_COUNTER_ADDR;

- Use Atomic Increment Instruction to implement the counter

scratch_incr(pkt_count);

__intrinsic void scratch_incr( volatile void __declspec(scratch) *address /* address to incr */ ) { INTRINSIC_BEGIN; { __asm scratch[incr, --, address, 0] } INTRINSIC_END; }

- The result is still correct while multiple ME are used

- Packet Size Counter

- The usage of packet counter and packet size counter

- The meta-data of the packet

typedef struct { dl_buf_handle_t dlBufHandle; // lw0 unsigned int buffer_next : 32; // lw1 unsigned int buffer_size : 16; // lw2 unsigned int offset : 16; unsigned int packet_size : 16; // lw3 unsigned int free_list_id : 4; unsigned int rx_stat : 4; unsigned int header_type : 8; unsigned int input_port : 16; // lw4 unsigned int output_port : 16; } ring_data_t3;

- Use Atomic Add Instruction to implement the counter

scratch_add(&pkt_size, byte_count, ctx_swap, &counter_sig);

void scratch_add( declspec(sram_write_reg) unsigned int *data, /* data to add */ volatile void __declspec(scratch) *address, /* address to add */ sync_t sync, /* type of synchronization to use */ SIGNAL *sig_ptr /* signal to raise upon completion */ ) {…}

- Multiple size of traffic are evaluated (64B, 128B, 256B)

- Show one of the performance limit of network processor (interface)

- Demo how to generate own packet traffic

- The format of STRM traffic is plain-text format

DIY-1. Multiple Port Packet Counter

Modify the above projects to:

- Generate three kinds of Ethernet-IP-TCP Packet Traffic (Size: 68B, 72B, 76B) (Each traffic has 10 packets)

- Assign Port 0 to 2 a packet stream (Port 0: 68B, Port 1: 72B, Port 2: 76B)

- Set Outgoing Port to Incoming Port Plus one

| Incoming Port | Outgoing Port |
| --- | --- |
| Port 0 | Port 1 |
| Port 1 | Port 2 |
| Port 2 | Port 0 |

- Count total size of packet pass through the three ports separately.

- Use the function of the workbench to verify the result

IXP Training Part 2 Outline

Second Hour

- IP Lookup Project – Linear Search Version

- Given a routing table with 4 entries:

| Entry # | Prefix | Port |
| --- | --- | --- |
| #1 | 0.0.0.0/0 | P0 |
| #2 | 140.116.0.0/16 | P1 |
| #3 | 140.116.82.0/24 | P2 |
| #4 | 140.116.246.0/24 | P2 |

- Suppose we have four packet with specific destination address field

| Packet # | Destination Address | Matched Prefix (Entry) | Port |
| --- | --- | --- | --- |
| Packet #1 | 140.116.82.28 | 140.116.82.0/24 (#3) | P2 |
| Packet #2 | 140.116.112.2 | 140.116.0.0/16 (#2) | P1 |
| Packet #3 | 140.112.101.111 | 0.0.0.0/0 (#1) | P0 |
| Packet #4 | 8.8.8.8 | 0.0.0.0/0 (#1) | P0 |

- Discuss the Longest Prefix Matching result

- Example data structure of a routing table entry

| Prefix (32) |
| --- |
| Length (16) | Port (16) |

- Script Format (Assume the base address is 0x40065080)

0x40065080 0x00000000

0x40065084 0x00000000

0x40065088 0x8C740000

0x4006508C 0x00100001

0x40065090 0x8C745200

0x40065094 0x00180002

0x40065098 0x8C74F600

0x4006509C 0x00180002

- The code to obtain the needed header fields

dram_read(&header, (__declspec(dram) unsigned int *) (Dl_BufGetData(rdata.dlBufHandle) + rdata.offset ), 5, sig_done, &sig_get_dram_header_pair); __wait_for_all(&sig_get_dram_header_pair);

- The Code of get an routing table entry

sram_read(&sram_entry, (__declspec(sram) entry *)(Base_1 + (loop*2*4)), 2, sig_done, &sram_sig_base1); __wait_for_all(&sram_sig_base1);

- The Code of Longest Prefix Matching (LPM)

if( ( sram_entry.length == 0 ) ¦¦ ( ( sram_entry.prefix >> (32-sram_entry.length) ) == (dip >> (32-sram_entry.length) ) ) ) { if( sram_entry.length >= default_length ) { default_length = sram_entry.length; port_out = sram_entry.port; } }

- Used pre-generated traffic to demo the functional

| Packet # | Result |
| --- | --- |
| Packet #1 | Send to Port 2 |
| Packet #2 | Send to Port 1 |
| Packet #3 | Send to Port 0 |
| Packet #4 | Send to Port 0 |

- Packet Classification Project – Linear Search Version

- Given a rule table with 5 rules (R1~R5)

- SA => Source Address; DA=> Destination Address (Prefix Matching)

- SP => Source Port; DP => Destination Port; (Range Matching)

- PO => Protocol (Exact Matching)

| # | SA | DA | SP | DP | PO | Action |
| --- | --- | --- | --- | --- | --- | --- |
| R1 | 140.116.82.19/32 | 140.116.82.28/32 | 0-65535 | 21 | 6 | Send to P2 |
| R2 | 140.116.82.28/32 | 140.116.246.0/24. | 1024 | 0-65535 | * | Send to P1 |
| R3 | 140.116.82.0/24 | 0.0.0.0/0 | 3321 | 80 | 7 | Send to P0 |
| R4 | 0.0.0.0/0 | 140.116.82.0/24 | 5432 | 139 | 6 | Send to P2 |
| R5 | 0.0.0.0/0 | 0.0.0.0/0 | 0-65535 | 0-65535 | * | Send to P3 |

- Suppose we have seven packets with follows header fields

| # | SA | DA | SP | DP | PO | Result ? |
| --- | --- | --- | --- | --- | --- | --- |
| P1 | 140.116.82.19 | 140.116.82.28 | 4324 | 21 | 6 | R1 (P2) |
| P2 | 140.112.32.24 | 140.113.23.22 | 3243 | 21 | 7 | R5 (P3) |
| P3 | 140.116.82.19 | 140.116.82.28 | 5432 | 139 | 6 | R4 (P2) |
| P4 | 140.116.82.28 | 140.116.246.77 | 1024 | 3579 | 3 | R2 (P1) |
| P5 | 140.116.82.32 | 140.116.82.19 | 3321 | 80 | 7 | R3 (P0) |
| P6 | 140.116.82.28 | 140.116.246.46 | 1024 | 4592 | 7 | R2 (P1) |
| P7 | 140.116.82.19 | 140.116.82.28 | 2211 | 21 | 6 | R1 (P2) |

- A simple data structure to store a rule

| SA (32) |
| --- |
| DA (32) |
| SP Begin (16) | SP End (16) |
| DP Begin (16) | DP End (16) |
| SA-LEN (8) | DA-LEN (8) | PO (8) | Rule ID (8) |

- Above rule table become

| R1 | 0x40065080 | 0x8C745213 |
| --- | --- | --- |
|  | 0x40065084 | 0x8C74521C |
|  | 0x40065088 | 0x0000FFFF |
|  | 0x4006508C | 0x00150015 |
|  | 0x40065090 | 0x20200602 |
| R2 | 0x40065094 | 0x8C74521C |
|  | 0x40065098 | 0x8C74F600 |
|  | 0x4006509C | 0x04000400 |
|  | 0x400650A0 | 0x0000FFFF |
|  | 0x400650A4 | 0x20180001 |
| R3 | 0x400650A8 | 0x8C745200 |
|  | 0x400650AC | 0x00000000 |
|  | 0x400650B0 | 0x0CF90CF9 |
|  | 0x400650B4 | 0x00500050 |
|  | 0x400650B8 | 0x18000700 |
| R4 | 0x400650BC | 0x00000000 |
|  | 0x400650C0 | 0x8C745200 |
|  | 0x400650C4 | 0x15381538 |
|  | 0x400650C8 | 0x008B008B |
|  | 0x400650CC | 0x00180602 |
| R5 | 0x400650D0 | 0x00000000 |
|  | 0x400650D4 | 0x00000000 |
|  | 0x400650D8 | 0x0000FFFF |
|  | 0x400650DC | 0x0000FFFF |
|  | 0x400650E0 | 0x00000003 |

IXP Training Part 2 Outline

Third Hour

DIY-2: Statistics Counter Project

主要目標: 計算每個Flow的封包數和位元組數

一般來說，Flow的定義是Source Address, Destination Address, Source Port, Destination Port, Protocol 皆一樣的不同封包.

這裡採用不同的定義, Flow被定義為Match 相同一條Rule的不同封包.

請採用下列的Rule Table作為分Flow的依據

| Rule # | SA | DA | Action |
| --- | --- | --- | --- |
| R1 | 192.0.0.0/1 | 0.0.0.0/1 | 0 |
| R2 | 0.0.0.0/0 | 0.0.0.0/1 | 1 |
| R3 | 192.0.0.0/1 | 0.0.0.0/0 | 2 |
| R4 | 0.0.0.0/0 | 0.0.0.0/0 | 3 |

因此總共會有4個Flow, 針對每個Flow, 需要去計算收到的封包數和位元組數。

請自行設計需要用到的資料結構。